## Slide 1: PDE 3802 AI in Robotics Week 2: Natural and Artificial Vision
Department of Design Engineering and Mathematics

## Slide 2: Electromagnetic spectrum
https://www.youtube.com/watch?v=lwfJPc-rSXw
Notes: What is special about visible light? Answer: Nothing is special about it. It is only special because we can see it.
The whole spectrum has different properties depending on the frequency.
Computer vision is based mostly based on it bt we can apply the techniques for visible light to infrared or radar. We can build sensors that can sense beyond human level.
We still favor visible freqwuency because we can interpret it.

## Slide 3: Visible light
https://www.youtube.com/watch?v=PMtC34pzKGc
Notes: 380-700nm wavelength
In computer vision we favor visible frequencies, because we can naturally interpret the results.
But we shouldn’t restrict our selves only to the visible frequencies.

## Slide 4: Eyes
Notes: To see things we use eyes, and many different types of eyes . With such different properties because of evolution, they were sort of adapted to different environment and situations.
They all do vision but they all do vision in very different ways. Spiders have many eyes.
Bottom left is a deep sea fish. Can you see the eyes (the transparent ones are the eyes) No light to see anything. It only looks up to get light from the surface.
In deep sea even a minor light can provide valuable information.
Bottom right is an insect with eyes far apart. Cover 160 degrees. Can see every where around. Also it can process independently.
Bottom middle is a reptile, a small lizard. What’s special about it? How many eyes does it have? It has 3 eyes. One on the top. It is not as accurate as the other two eyes. It is essentially a Light sensor.

## Slide 5: Human eye and photoreceptors
https://www.youtube.com/watch?v=hsh2kPdgazo
Notes: Do you remember your biology classes from high school?
There are some aspects that are of more interest to us, besides actual compositon, physiology or geometry of the eyes, what’s of more interest to us are the sensors,
The sensors are the cones and the rods. (black and white) We only see the center precisely, the fovia. We only have color vision on the cones.
At night we mostly see black and white. Rods are more sensitive to faint light.
How many types of cones do you have? How many color components do we have? Answer: We have three cones.

## Slide 6: Colour spectrum and human rods
Notes: Our sensors are particularly good at detecting RGB, that’s why we use that. So we have three cones.
X axis: wavelength Y axis: absorption. How much each cone is sensitive to that type of light.
Certainly there is overlapping so that we can see all of them but with different amount..
Each person has their peaks at slightliy different points.
People who are color blind have these two RG peaks too close so that they dont have the capability to distinguish them.
There are different types of color blindness. Some people have two cones.

## Slide 7: Photoreceptors in different species
Notes: Dogs only have two cones. Many mammals only have two cones. They don’t see all the shades that we can see.
Birds have 4 types of cones. One cone is in the UV. We don’t. It is like a superpower.

## Slide 8: Animal vision
http://www.nhm.ac.uk/discover/how-do-other-animals-see-the-world.html
http://designtaxi.com/news/381848/Watch-Fascinating-Look-At-How-Cats-Snakes-Other-Animals-See-Our-World/
Notes: We can see other types of vision. This is just an interpretation. We can not see like they see.
Birds have very acute and high resolution vision. But color processing is beyond our comprehension.
Cats, have reduced color range, same for dogs.
Snake , this is a standart representaton of infrared. We are not sure how they see exatly.
Sharks and fish, reduced color, high sensitivity to light.
Rat vision, whats special. Their eyes move independetly, two focus.

## Slide 9: Reactive vision (e.g. drosophila fly)
Compound eyes
Eight photoreceptors arranged in a regular pattern: automatic “map building”
Poor spatial quality and light sensitivity but extremely fast, almost omnidirectional, movement detection
Notes: Type of vision that insects have. is quite related to the type of vision that the robots might have.
Ancient robots have the sensory processing that is much akin to that of the insects.
It is sort of an automatic map. Insects have very tiny not very elaborate central nervous system. They don’t do a lot of brain processing.
The have a sort of distributed nervous system where the central nervous system process in a parallel way and directly connected to the actuator.
If something is sensed, the insect has an instinct of moving to the opposite direction. No object recognition, no multilayer of neurons. It is a reactive vision.
That’s why the flies are hard to catch, it is a lot more effective and useful to just move away.
They don’t see the window, they just see the light and hit the window 1000 times, without learning.
In robots for obstacle avoidance, you may want to use such a system. You don’t have to classify the obstacle.

## Slide 10: Electromagnetic Spectrum

## Slide 11: Inside a Human eye
https://www.youtube.com/watch?v=eySkNWTI03Q

## Slide 12: Animal vision
https://youtu.be/VphtcDhHj40
Notes: Pigeons have much better vision than humans
Snakes have infrared receptors
Cows don’t see color red. They have near panoramic vision
Horses can’t see directly in fron of them
Fishers have an ultraviolet receptors, sharks can’t distinguish colors
Birds have ultraviolet sensing can differentiate males and females.
Many animals can’t see red
Frogs only sense moving things
Some reptiles have two eyes that are independent

## Slide 13: Eye evolution
A human eye could have evolved in just 400000 generations (less than 10 million years)
Every step conveys a clear advantage over the previous one (no implausible “jumps” )
Notes: Every step in evolution gave an advantage to the rpevious one.
Simple light sensor
Then, the retina starts to bend. Then not only you can detect the changing light, but also where it is coming from. You have increased FoV and Res
Then fovia is evolved, for a precise and powerful vision in a tiny spot.
All these types of exist in different animals.
Lesson for robotics: Each of them might be useful. A less powerful sensor is sometimes better. You don’t have to use a camera for everything. Complex sensor are very costly.
You get more data with more advanced sensors and it is costly to process.

## Slide 14: Eye evolution: human vs. octopus
Advantages and disadvantages of “inside out” retina
Retina
Nerve fibres
Optic nerve
Blind spot
Notes: Similarity between human and octopus eyes. They have evolved completely independetly. Because eyes have evolved later.
Yet they evolved very similarly. This is accidental convergence.
Human nerves are in front of the sensors. Octopus: nerves are bhind the sensors. Octopus don’t have blind spots.
Which one is better. ? Maybe the octopus. Bu the nerves give somehow protection for sensors maybe good for us. Still maybe the octopus is more preferable.

## Slide 15: Vision in the brain
https://www.youtube.com/watch?v=P-7mO2FhaVE
Notes: Vision problem is ill posed, because we can see 2D but the world is 3D
Secondly, our eyes are evolved to find food and escape from danger. Not to assess artistic images
Right side of FoV is processed by the left brain. There is a crossing on the brain.
Otherwise stereo vision would not be possible. Two parts would process independently.

## Slide 16: Visual processing in the human cortex
In simpler animals visual cells do most of the job: complex visual sensors and simple brain.
In vertebrate (e.g. humans) the brain cortex does most of the job: (relatively) simple visual sensor and complex brain.
Notes: A lot of our brain is dedicated to vision

## Slide 17: What is vision?
Object recognition?
Notes: Should we keep the biological system the same or should we change them?
You can see two things but not at the same time (two heads and a vase) (rabbit or duck)
Look at the right. Looks quite like an elephant, but it has so many legs. Still at first sight we see it as an elephant.
We are used to see things noisy, distorted and with occlusions, but we still can recognize them. our vision is not photographic.

## Slide 18: What is vision?
Size estimation?
Notes: Have you seen this illusion. Distances don’t look the same but they are the same.
The bottom one is an unusual shape. We are not used to seeing such things. They definitely don’t look parallel , but they are completely parallel.

## Slide 19: What is vision?
Colour perception?
Notes: What about color , what do you see? It seems color is changing, but actually it is not. This is because of the background.
In our visual cortex, there are neurons that enhance contrast

## Slide 20: What is vision?
Movement detection?
Notes: Look at this dancer. Look in the middle . Which direction is she turning? If you look left and center, and then right and center. Its because of the occlusion.
The side images have lines that create occlusion but they work only in one direction.

## Slide 21: What do we see?
Notes: Looks like a man or something. It’s just a bunch of 9 dots.

## Slide 22: The importance of visual attention
https://www.youtube.com/watch?v=vJG698U2Mvo
Notes: We see what we need to see. We don’t see photographic, we don’t analyze an image, we only see what we need to see

## Slide 23: The social bias
https://www.youtube.com/watch?v=8FIEZXMUM2I
Notes: What did you see? The shape didn’t matter right? They seemed like human that have emotions or feelings. You can feel anger, or happiness or rage.
We are social animals

## Slide 24: Buba vs. Kiki
Notes: What about language which one is Buba and which one is Kiki?
80% of the people think the left is KİKi and right is Buba. Majority of the people tend to see it in a certain way. We tend to call things according to their aspect.

## Slide 25: Summary: What affects what we see?
Attention
Goals
Knowledge of the world
Language associations
Other senses
Context
Mood and drives
Social environment
…
Notes: We’ve seen a review of many things. The main message is that vision is not photographic.
Our vision is affected by our attention. If you’re trying to find somewhere to eat. You will see restaurants. If you are worried that someone might find you, you will be aware of certain type of inputs both visual and audial.
Everything you know, will affect the way you perceive things. Your experience will make you see things differently.
Language association: We have seen that how we use language closely identify things and other the other way around, other senses, of course.
Sound especially sound is very, very integrated with the vision. Because they are the two most far away senses, smell and taste are far closer.
Smell and taste, are also related to vision and then can all modify the way we see things.
The context might mean many things: You can see things differently yourself, according to the situation, so the same picture, or the same name is an essential question or the same scenari

## Slide 26: Plenty more illusions
http://brainden.com/optical-illusions.htm
The bottom line:
This is how we really see, not just “illusions”
Notes: So. yeah here you have a link to more illusions and important things that Okay, these are sort of visual games right but that's how our vision really works.
Okay, we really see the way we've analyzed all this time here this really happens all the time, and this always makes me think right, how we can.
We still trust witnesses so much in many cases. That was our perception if there are Social and emotional aspects involved.
Our perception is really not reliable.

## Slide 27: Should artificial vision be like natural vision?
Objectives
Reliability
Sensors
Complexity
Flexibility
Speed
Other sensory modalities
Attention
Notes: And that raises the question.
So should artificial vision be like natural vision.
Yes, I tend to agree with the fact that building a Multi purpose artificial vision, would have to be biased in order to act a more like a natural vision.
However, if you want to do, specific purpose artificial vision, you would have to eliminate those biases in order to achieve a certain level of accuracy, but then you'd have to pay with the cost of not being able to be as natural as it could be.
So, if it is a social robot maybe you want a robot that think more like human that falls into some illusions as well. It would make it closer to the humans, if it was feeling and the perceiving in a more similar way, if you want a robot for waste sorting the right then you want it to recognize the trash with 99.9% accuracy.
Okay, so they are two completely different tasks they both you use artificial vision in very different ways. Natural visual is multipurpose
But, in general, the general artificial systems are focused, they have Only one or very few objectives and they are designed to solve a specific problem they are not usually for general purpose.
Even for the social robot will probably not need to do, waste sorting and the other way around. So there is hardly the need to implement the both ways of processing into the same system, why should I do that.
Okay, what about reliability. Usually with a natural vision that might be okay illumination issues you might trick the system Okay, but in the domain and visual condition for which the system was developed, It should be very, very reliable.
Sensors: cameras now are very powerful when compared with human eye. You can have 50 megapixel camera very cheaply on the phone. And you can zoom in much better than our eyes, can compensate for illumination easily. Artificial sensor can work better.
Flexibility: is the opposite of having focused objectives , we probably don't want the flexibility. We want to solve a specific problem in a very reliable, very precise and very consistent way. In the future, perhaps. For systems that can do two or three things at a time, then Okay, they might become are flexible at this stage, in time, we are not doing that.
The relation to other sensory modalities that's something that is solely under development in my opinion, and we should be working a lot more researchers on integrating different modalities
Finally, attention, we do have that we have a very attention based sensing than artificial visual systems. That focus their resources on some specific things because you can imagine it's very costly to process a bigger image and try to analyze every bit of it for every frame, so we do have attention systems that allow us to optimize the resources you use to perceive things in the way that is more suitable to the task. Metaverse and augmented reality can take a lot from attention based natural vision, because Processing and transmitting 360 degrees of vision and all the 5 senses is very costly.

## Slide 28: What can Computer Vision do for Robotics?
Accurate Robot-Object Positioning
Keeping Relative Position under Movement
Visualization / Teaching / Telerobotics
Performing measurements
Object Recognition
Action recognition
…
Notes: How do we use computer vision robotics well , nowadays in so so many different things. that are almost no robots without vision, for example If you are to interact with the object selecting matching and manipulate, you need to. İdentify where it is, orientation distance to be able to approach it and take it or move it correctly.
If you have a mobile robot You need to localize yourself and vision is very powerful that obstacle avoidance identify the area path , planning they're all based very much on vision, but not only, you can use a infrared sensor, lidar but almost always be integrated with vision as well.
We can use it with the robotics For visualizing, you can use augmented reality with robot.
In teaching, not only for teaching robotics but for robot used to interact with humans as a partner, so understanding what's happening and creating a context.
Measuring things which means again Assessing the state of the environment in many different ways and then obviously recognizing objects recognizing people and what they are doing.
You might have a robot that recognize objects and what the person is doing to interact with the person through but in there, these are focused tasks right, then they are processed.

## Slide 29: What other senses can we use?
Sound (speech recognition, localisation, object identification)
Pressure/touch (object recognition, human)
Chemical (detect air or soil composition, e.g. dangerous gas)
Infrared (obstacle avoidance, distance estimation)
Radar/sonar/lidar (distance estimation, mapping, recognition)
Many more…
Notes: Sound: microphone
Pressure/touch: Piezo electric sensors
Chemical sensors
Infrared: distance, obstacle
radar,/sonar/lidar

## Slide 30: Introduction

## Slide 31: 1.1 What is Computer Vision

## Slide 32
Researchers in computer vision have been developing, in parallel, mathematical techniques for recovering the three-dimensional shape and appearance of objects in imagery.
Many applications
Difficult problem (inverse problem)
    Forward model: how objects move and animate, how light reflects off their surfaces etc.
Visual world is more complex than sound

## Slide 33: Applications
Optical character recognition (OCR)
Machine inspection
Retail
Warehouse logistics
Medical imaging
Self-driving vehicles
3D model building (photogrammetry)
Match move
Motion capture (mocap)
Surveillance
Fingerprint recognition and biometrics
Notes: *Optical character recognition (OCR): reading handwritten postal codes on letters (Figure 1.4a) and automatic number plate recognition (ANPR);
*Machine inspection: rapid parts inspection for quality assurance using stereo vision with specialized illumination to measure tolerances on aircraft wings or auto body parts (Figure 1.4b) or looking for defects in steel castings using X-ray vision;
* Retail: object recognition for automated checkout lanes and fully automated stores (Wingfield 2019);
• Warehouse logistics: autonomous package delivery and pallet-carrying “drives” (Guizzo 2008; O’Brian 2019) and parts picking by robotic manipulators (Figure 1.4c; Ackerman 2020);
• Medical imaging: registering pre-operative and intra-operative imagery (Figure 1.4d) or performing long-term studies of people’s brain morphology as they age;
• Self-driving vehicles: capable of driving point-to-point between cities (Figure 1.4e; Montemerlo, Becker et al. 2008; Urmson, Anhalt et al. 2008; Janai, G¨uney et al. 2020) as well as autonomous flight (Kaufmann, Gehrig et al. 2019);
• 3D model building (photogrammetry): fully automated construction of 3D models from aerial and drone photographs (Figure 1.4f);
• Match move: merging computer-generated imagery (CGI) with live action footage by tracking feature points in the source video to estimate the 3D camera motion and shape of the environment. Such techniques are widely used in Hollywood, e.g., in movies such as Jurassic Park (Roble 1999; Roble and Zafar 2009); they also require the use of precise matting to insert new elements between foreground and background elements (Chuang, Agarwala et al. 2002).
• Motion capture (mocap): using retro-reflective markers viewed from multiple cameras or other vision-based techniques to capture actors for computer animation;
• Surveillance: monitoring for intruders, analyzing highway traffic and monitoring pools for drowning victims (e.g., https://swimeye.com);
• Fingerprint recognition and biometrics: for automatic access authentication as well as forensic applications.

## Slide 34
Notes: Some industrial applications of computer vision:
optical character recognition (OCR), http://yann.lecun.com/exdb/ lenet;
mechanical inspection, http://www.cognitens.com;
warehouse picking, https://covariant.ai;
medical imaging, http://www.clarontech.com
self-driving cars, (Montemerlo, Becker et al. 2008) © 2008 Wiley;
drone-based photogrammetry, https://www.pix4d.com/blog/mapping-chillon-castle-with-drone.

## Slide 35: Consumer Applications
Stitching
Exposure bracketing
Morphing
3D modeling
Video match move and stabilization
Photo-based walkthroughs
Face detection
Visual authentication
Notes: Stitching: turning overlapping photos into a single seamlessly stitched panorama (Figure 1.5a), as described in Section 8.2;
• Exposure bracketing: merging multiple exposures taken under challenging lighting conditions (strong sunlight and shadows) into a single perfectly exposed image (Figure 1.5b), as described in Section 10.2;
• Morphing: turning a picture of one of your friends into another, using a seamless morph transition (Figure 1.5c);
• 3D modeling: converting one or more snapshots into a 3D model of the object or person you are photographing (Figure 1.5d), as described in Section 13.6;
• Video match move and stabilization: inserting 2D pictures or 3D models into your videos by automatically tracking nearby reference points (see Section 11.4.4)2 or using motion estimates to remove shake from your videos (see Section 9.2.1);
• Photo-based walkthroughs: navigating a large collection of photographs, such as the interior of your house, by flying between different photos in 3D (see Sections 14.1.2 and 14.5.5);
• Face detection: for improved camera focusing as well as more relevant image searching (see Section 6.3.1);
• Visual authentication: automatically logging family members onto your home computer as they sit down in front of the webcam (see Section 6.2.4).

## Slide 36
Notes: Some consumer applications of computer vision:
image stitching: merging different views (Szeliski and Shum 1997) © 1997 ACM;
(b) exposure bracketing: merging different exposures;
(c) morphing: blending between two photographs (Gomes, Darsa et al. 1999) © 1999 Morgan Kaufmann;
(d) smartphone augmented reality showing real-time depth occlusion effects (Valentin, Kowdle et al. 2018) © 2018 ACM.

## Slide 38: 1.2 Brief History
1970’s
    Visual perception component of an agenda to mimic human intelligence
    3D reconstruction, full scene understanding
    Edge extraction, line labeling, pictorial structures, generalized cylinders, intrinsic images, surface orientation, shadows, optical flow, camera motion
1980’s
    Image pyramids: image blending, coarse to fine correspondence
    Wavelets, Shape from shading, Shape from texture, Shape from focus, Contour tracking, Markov random field, Kalman filters
1990’s
    Structure from motion, dense stereo matching, multiview reconcstruction, face tracking, image segmentation, face recognition (PCA, )
    Image rendering,
Notes: According to one well-known story, in 1966, Marvin Minsky at MIT asked his undergraduate student Gerald Jay Sussman to “spend the summer linking a camera to a computer and getting the computer to describe what it saw” (Boden 2006, p. 781).5 We now know that the problem is slightly more difficult than that.
Digital image processing already existed
Computer vision is distinguished from digital image processing as a desire to recover the three-dimensional structure of the world from images and to use this as a stepping stone towards
full scene understanding.

## Slide 39
Notes: Line labeling: Junctions (forks) are labeled in order to recognize different 3D scenes
Pictorial structures: visual objects are described by breaking down the object into a number of more "primitive parts," and by specifying an allowable range of spatial relations which these "primitive parts" must satisfy for the object to be present.
articulated body model (Marr 1982): One popular approach used generalized cylinders, i.e., solids of revolution and swept closed curves, often arranged into parts relationships. In robotics and computer animation, these linked-part graphs are often called kinematic chains
İntrinsic images (Barrow and Tenenbaum 1981): Intrinsic Image Decomposition is the process of separating an image into its formation components such as reflectance (albedo) and shading (illumination)
stereo correspondence (Marr 1982): Stereo correspondence establishes matches between the left and right rectified images to produce a disparity map. A disparity map is a 2D image that uses grayscale values to indicate the disparity, or distance, between features in left and right rectified images.
(optical flow (Nagel and Enkelmann 1986: Optical flow is a technique used to describe image motion. It is usually applied to a series of images that have a small time step between them, for example, video frames. Optical flow calculates a velocity for points within the images, and provides an estimation of where points could be in the next image sequence.

## Slide 40
Notes: pyramid blending (Burt and Adelson 1983b): pyramid: a signal or an image is subject to repeated smoothing and subsampling, image blending with Pyramids gives you seamless blending without leaving much data in the images.
shape from shading (Freeman and Adelson 1991): Shape-from-Shading models show how a light source interacts with an object, establishing the relationship between surface normals and intensity of reflected light
edge detection (Freeman and Adelson 1991): includes a variety of mathematical methods that aim at identifying edges, defined as curves in a digital image at which the image brightness changes sharply or,
Physically based models (Terzopoulos and Witkin 1988): Physically-based modeling adds new levels of representation to graphics objects. In addition to geometry — forces, torques, velocities, accelerations, kinetic and potential energies, heat, and other physical quantities are used to control the creation and evolution of models.
regularization-based surface reconstruction (Terzopoulos 1988) :
range data acquisition and merging

## Slide 41
Notes: Factorization based structure from motion (Tomasi and Kanade 1992) : The factorization method has been demonstrated to be a powerful approach to extracting structure and motion from image sequences
dense stereo matching (Boykov, Veksler, and Zabih 2001), : Dense stereo correspondence is one category of matching methods, which, normally, operates at pixel level in order to reconstruct 3D views of the real world
multi-view reconstruction (Seitz and Dyer 1999) : The goal of multiview 3D reconstruction is to infer geometrical structure of a scene captured by a collection of images.
face tracking (Matthews, Xiao, and Baker 2007): real-time information on eye movement and closure, gaze direction, 3D and 2D pupil coordinates, and iris radius.
image segmentation (Belongie, Fowlkes et al. 2002) : Image segmentation is a commonly used technique in digital image processing and analysis to partition an image into multiple parts or regions, often based on the characteristics of the pixels in the image.
face recognition:

## Slide 43: 1.2 Brief History
2000’s
    Data driven feature based learning approaches
    Increased availability of immense quantities of labeled images
    ImageNet
2010’s
    GPU’s, AlexNet
    Open source neural network models
    Action recognition, pose estimation
    The Microsoft Kinect depth camera
    panoramic image stitching and bracketed high dynamic range image merging
    simultaneous localization and mapping (SLAM)
    visual inertial odometry (VIO)

## Slide 44
Notes: image-based rendering (Gortler, Grzeszczuk et al. 1996),: image-based modeling and rendering (IBMR) methods rely on a set of two-dimensional images of a scene to generate a three-dimensional model and then render some novel views of this scene.
image-based modeling (Debevec, Taylor, and Malik 1996) : for automatically creating realistic 3D models from collections of images were also being introduced
interactive tone mapping (Lischinski, Farbman et al. 2006) : Interactive tone mapping allows users to adjust the appearance of an image in real-time, often through a graphical user interface or interactive controls. This can be particularly useful when dealing with HDR content, where there is a significant difference in brightness between the darkest and brightest parts of an image.
texture synthesis (Efros and Freeman 2001): Texture synthesis is a computer graphics technique that involves creating or generating textures, which are patterns or images that can be repeated seamlessly. The goal is to create textures that appear realistic and have certain characteristics, such as color, shape, and structure, similar to those found in natural or real-world materials.
feature-based recognition (Fergus, Perona, and Zisserman 2007): Feature-based recognition refers to a process in computer vision and computer-aided design (CAD) where the identification and analysis of specific features within an object or scene are used for recognition and understanding.1) Feature Extraction 2) Feature Matching 3) Object Recognition
region-based recognition (Mori, Ren et al. 2004: Region-based recognition is a concept in computer vision and image processing where objects or structures are identified and understood based on the analysis of regions within an image. Instead of focusing on individual features like edges or corners, region-based recognition considers larger, coherent regions that may correspond to distinct objects or meaningful parts of a scene.

## Slide 45
Notes: the SuperVision deep neural network © Krizhevsky, Sutskever, and Hinton (2012); More commonly known as AlexNet. AlexNet is a convolutional neural network (CNN) architecture that gained significant attention and played a crucial role in advancing the field of deep learning and computer vision. It was developed by Alex Krizhevsky, Ilya Sutskever, and Geoffrey Hinton, and it won the ImageNet Large Scale Visual Recognition Challenge (ILSVRC) in 2012.
object instance segmentation (He, Gkioxari et al. 2017) : Object instance segmentation is a computer vision task that involves identifying and delineating individual objects within an image, providing a pixel-level mask for each object instance. In other words, it goes beyond object detection (which identifies object bounding boxes) and object classification (
whole body, expression, and gesture fitting from a single image (Pavlakos, Choutas et al. 2019) :
fusing multiple color depth images using the KinectFusion real-time system 2011: KinectFusion refers to a real-time 3D reconstruction technique that utilizes depth information captured by the Microsoft Kinect sensor. Key features 1) Depth Sensing 2) Volumetric Representation: 3)Camera Pose Estimation 4) Integration and Ray Casting: to project the model back into the depth images. 5) Real-Time Reconstruction: KinectFusion is designed to operate in real-timeApplications: 1) 3D Scanning: Creating 3D models of physical objects 2) Augmented Reality: Combining real-world scenes with virtual objects 3) Robotics: Providing robots with the ability to perceive and navigate their environment in 3D.
smartphone augmented reality with real-time depth occlusion effects (Valentin, Kowdle et al. 2018) :
3D map computed in real-time on a fully autonomous Skydio R1 drone:

## Slide 46
Notes: Computational photography is a field of study and technology that combines computational methods with traditional photography to enhance or extend the capabilities of imaging systems. It leverages computational techniques to improve various aspects of image acquisition, processing, and manipulation, going beyond the limitations of conventional optics and sensors. Computational photography encompasses a wide range of techniques and applications, and its goal is often to create images that would be challenging or impossible to capture with traditional cameras alone.

## Slide 48: Setup for the course
Download and Install Anaconda
Create a virtual environment (different files depending on your OS)
Open JupyterLab
Work with both notebooks and .py scripts with JupyterLab
https://www.anaconda.com/download/

## Slide 49: Choose your operating system

## Slide 50: Choose you operating system

## Slide 51
Remove any spaces in the username
Add Anaconda to my Path environment variable
After installation we now need to download the libraries used for this course.
The installation has installed the Anaconda Prompt command line tool.
We’ll be using it for these next step
Create a new environment
Install JupyterLab and Jupyter Notebook in this environment

## Slide 52: Numpy Arrays
Open 00-NumPy-Arrays
Run the line by shift-enter
Arrays
    Numpy:
    List
    Np.array
    Np.arange
    Np.zeros, np.ones
Operations
    Np.random.randint
    We can use the following on numpy arrays
      Max, min, mean, argmin, argmax, reshape
      Np.arange.reshape

## Slide 53: Images and Numpy
from PIL import Image
import matplotlib.pyplot as plt
    Image.open
    np.asarray(pic)
    pic_arr.shape: (1300,1950,3) shape
    plt.imshow(pic_arr)
    pic_red = pic_arr.copy(), pic_red[:, :, 1] = 0 , pic_red[:, :, 2] = 0

## Slide 54: OpenCV
Open Anaconda Prompt
Type (or paste):
conda install opencv
pip install opencv-python
This should install OpenCV 4 (.7 latest stable version)

## Slide 55: Some resources
  On-line Computer Vision Compendium (University of Edinburgh):
  http://homepages.inf.ed.ac.uk/rbf/CVonline/
  Comprehensive list of computer vision methods:
  https://sites.google.com/site/cvonlinewiki/home/generic-computer-vision-methods
  OpenCV tutorials:
  https://docs.opencv.org/4.5.0/d9/df8/tutorial_root.html
  Image processing in OpenCV (but not only):
  https://docs.opencv.org/4.5.0/d2/d96/tutorial_py_table_of_contents_imgproc.html
    In OpenCV, make sure you are looking at the Python code, not C++